## Slide 1: A Unified Framework for Traffic State Prediction and Class-Wise Speed Estimation in Mixed Traffic Conditions
Dr. Abirami Krishna Ashok
Dr.Bhargava Rama Chilukuri
Paper I.D: 8805

## Slide 2: Motivation: Homogeneous vs. Mixed Traffic
Mixed traffic
Seepage of smaller vehicles
Kinematic disparities
Substantial lateral movement
Staggered following
Need for mixed traffic conditions state characterisation, estimation, and prediction that captures vehicle class-specific behaviours and features
Introduction | Background | Methodology | Results | Contributions | Applications
State := f(v*)
State:= f(v1,v2,v3,…,vn)
Traffic state estimation (TSE): Inference of steady state traffic conditions using variables such as
  Flow, Density, Speed, , Travel Time, etc., for midblocks
  Queue length, Delay, etc., for intersections

## Slide 3: Conceptual Background
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 4: Analysis of observed speed patterns
U=2
U=3
U | # of traffic states | Configuration | Possible combinations | Total patterns
1 | 12 | (3) | 12 * 1 | 12
2 | 11 | (1,2), (2,1) | 11*6 | 66
3 | 10 | (1,1,1) | 10*6 | 60
Total |  |  |  | 138
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 5: Class-bin probabilities for Predominant Patterns (PP)
Class-bin probabilities for U=2
Class-bin probabilities for U=3
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 6: Class-bin probabilities for Non-Predominant Patterns (NPP)
Class-bin probabilities for U=2
Class-bin probabilities for U=3
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 7: Class-wise Speed Estimation Methodology
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 8: State prediction
Introduction | Background | Methodology | Results | Contributions | Applications
70 %
0.68
Overall accuracy
Macro F1 score
Model performance:

## Slide 9: Class-wise speed estimation approaches
1
Point Estimate (Joint Maximum a Posteriori, MAP)
2
Expected Value Rounding (EV)
3
Distribution-Preserving (DP) Allocation
Pattern with highest probability
1-1-2
3W: (0.43*21) + (0.24*27) + (0.33*25.02) = 23.77 kmph
2W: (0.43*21) + (0.24*27) + (0.33*25.02) = 23.77 kmph
CAR: (0.43*27) + (0.24*27) + (0.33*22.02) = 25.36 kmph
Vehicle class | Expected speed | Expected bin | Expected bin index
3W | 23.77 | 18-24 | 1
2W | 23.77 | 18-24 | 1
CAR | 25.36 | 24-30 | 2
Vehicle class | Bin 1 | Bin 2
3W | 0.43+0+(0.33*0.33) =0.54 | 0+0.24+(0.33*0.67) =0.46
2W | 0.43+0.24+(0.33*0.33)=0.78 | 0+0+(0.33*0.67)=0.22
CAR | 0+0+(0.33*0.83)=0.27 | 0.43+0.24+(0.33*0.17)=0.73
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 10: Analysis of Estimation Approaches Across Representative States
State | Point Estimate | Expected Value | Distribution Preserving | Ensemble Voting
16 | 1-1-2 | 1-1-2 | 1-1-2 | 1-1-2
21 | 1-1-2 | 1-1-2 | 1-1-2 | 1-1-2
36 | 1-1-2 | 1-1-2 | 1-1-2 | 1-1-2
41 | 1-2-2 | 1-1-2 | 1-2-2 | 1-2-2
27 | 1-2-3 | 1-3-2 | 1-2-3 | 1-2-3
37 | 1-3-2 | 1-3-2 | 1-3-2 | 1-3-2
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 11: Key Contributions
Class-wise Inference from Raw Data
Developed a probabilistic model to infer class-wise speeds (2W, 3W, cars) from unclassified vehicle-level data.
Bridges the gap between raw, mixed traffic data and class-sensitive insights for planning and operations.
Unified Modelling Framework
Integrated Clustering (GMM) + Prediction (Linear Regression, MLP) + Probabilistic Mapping.
Explicitly captures vehicle-class heterogeneity, overcoming traditional lane-based, homogeneous assumptions.
Multi-Method State Identification
Proposed and evaluated 3 complementary approaches: → Point Estimation (direct interpretability) → Expected Value (smooths variability) → Distribution-Preserving (retains probability shape)
Adopted an ensemble voting strategy to yield a robust, consensus traffic state.
Dual-Level Representation
Linked aggregate traffic states with class-specific speeds, providing: → Macro-level flow insights and → Micro-level vehicle-class behavior.
Enhances interpretability and real-world operational relevance.
1
2
3
4
Introduction | Background | Methodology | Results | Contributions | Applications

## Slide 12: Integration into ITS
Adaptive Signal Control
  Adjust signal phases/cycles based on predicted states.
  Enable class-based priority (e.g., buses, freight vehicles).
Congestion Pricing or Demand Management
  Use class-specific speeds and congestion probabilities for dynamic pricing.
  Implement access control during severe congestion.
Traffic Simulation and Control Evaluation
  Feed class-wise speed distributions into real-time simulation models.
  Evaluate and optimize signal control and routing strategies.
Traveler information Systems
  Integrate near-term class-wise speed forecasts into route guidance tools.
  Enhance information accuracy and traveler trust.
1
2
3
4
Introduction | Background | Methodology | Results | Contributions | Applications
Source: Google images

## Slide 13
Thank You
Abirami.K@themint.space
Dr.Abirami Krishna Ashok
Senior Project Officer
The MInT Colloborative Space, IIT Madras
Turning traffic data into meaningful mobility insights.